## Slide 1: SWIM Short Course SEAWAT Concepts
2016 Salt Water Intrusion Meeting
June 28 – July 1, 2016
Cairns, Australia

## Slide 2: SEAWAT Computer Program
Finite difference
Combined version of MODFLOW and MT3DMS
Designed to simulate transient, three-dimensional, fully saturated, variable-density groundwater flow

## Slide 3: Approaches for Representing Variable-Density Flow
Ignore it!
Sharp interface approach
Fully coupled flow and dispersive transport approach

## Slide 4: Classes of Variable-Density Models
Sharp Interface Approach
  Fast
  No dispersion
Dispersed Interface Approach
  Can predict changes in concentration
  Represent free convection processes
  Slow

## Slide 5: Why use SEAWAT?
Accurate
Documented
Public domain
Relatively easy to use
  Based on MODFLOW and MT3D
  Modular—Process/Package approach
Compatible with existing pre and post processors
Compatible with a wide range of utility programs (MODPATH, ZONEBUDGET, etc)

## Slide 6: Documentation
Version 1
Guo, W., and Bennett, G.D., 1999, SEAWAT Version 1.2: A computer program for simulations of groundwater flow of variable density: Eastern Tech, Cape Coral, Florida.
Version 2
Guo, W., and Langevin, C.D., 2002, User’s guide to SEAWAT: A computer program for simulation of three-dimensional variable-density ground-water flow: U.S. Geological Survey Techniques of Water Resources Investigations Book 6, Chapter A7, 79 p.
Version 3
Langevin, C.D., Shoemaker, W.B., and Guo, Weixing, 2004, MODFLOW-2000, the U.S. Geological Survey Modular Ground-Water Model–Documentation of the SEAWAT-2000 Version with the Variable-Density Flow Process (VDF) and the Integrated MT3DMS Transport Process (IMT): U.S. Geological Survey Open-File Report 03-426, 43 p.
Langevin, C.D., and Guo, W., 2006. MODFLOW/MT3DMS-based simulation of variable density ground water flow and transport: Ground Water vol. 44, no. 3:339-351.
Version 4
Langevin, C.D., Thorne, D.T., Dausman, A.M., Sukop, M.C., and Guo, Weixing, 2008, SEAWAT Version 4: A computer program for simulation of multi-species solute and heat transport. U.S. Geological Survey Techniques and Methods Book 6, Chapter A22, 39 p.

## Slide 7: Public Domain
http://water.usgs.gov/ogw/seawat

## Slide 8: SEAWAT Concept
Combine MODFLOW and MT3DMS into a single program
  Insert MT3DMS into MODFLOW main program
Modify MODFLOW routines to solve the variable-density groundwater flow equation

## Slide 9: Fluid Density (r)
Total Mass (fluid and salt) / Volume
Dimensions [ML-3]
Commonly denoted with r
Typical Values for Water
  Fresh: r = 1000 kg/m3; r = 62.43 lbs/ft3
  Seawater: r = 1025 kg/m3; r = 64.00 lbs/ft3

## Slide 10: Solute Concentration (C)
Solute mass fraction (w)
  Mass of solute / total mass of fluid
Solute volumetric concentration (C)
  Mass of solute / volume of fluid
Relation: C = r * w

## Slide 11: Head-Based Formulation?
Many variable-density codes solve equations in terms of pressure, but equations can also be formulated using head
Why head instead of pressure?
  Perhaps more intuitive
  Use popular codes, such as MODFLOW?
Complication: what is “head” in a variable-density system?

## Slide 12: Measures of Head
piezometer filled
with freshwater
piezometer filled
with aquifer water
at well opening
piezometer filled
with adjacent aquifer water
freshwater
brackish water
seawater
h
hf
he
point-water
head (h)
freshwater
head (hf)
environmental
head (he)

## Slide 13: Point-Water and Freshwater Head
A
B
Piezometer filled
with freshwater
Piezometer filled
with saline water
Datum
N
h: head
hf: equivalent freshwater head
P: pressure
: density
 f : density of freshwater
g: gravity
Z: elevation

## Slide 14: Converting between hf and h

## Slide 15: Why use hf in SEAWAT?
Conceptually straightforward (i.e. for freshwater system, hf = h)
Finite-difference form of governing equation can be solved by MODFLOW (with a few modifications)

## Slide 16: Darcy’s Law
pressure and permeability
equivalent freshwater head and hydraulic conductivity
can assume

## Slide 17: Governing Equation for Variable-Density Flow
or

## Slide 18: Governing Equation for Solute Transport
ADV
DSP
SSM
RCT

## Slide 19: Equation of State
Equation of state is used to relate fluid density to pressure, temperature, and concentration
Most rigorous form:
  r = r 0exp[BP(P-P0) + BT(T-T0)+BC(C-C0)]
  BP = 1/ r*dr/dP|T,C (fluid compressibility)
  BT = 1/ r*dr/dT|P,C (fluid coefficient of thermal expansion)
  BC = 1/ r*dr/dC|P,T (slope of fluid density as a function of solute concentration, divided by reference density)
A linear approximation is often used, which can be written as:
  r = r 0[1 + BP(P-P0) + BT(T-T0)+BC(C-C0)], or
  r = r 0+ dr/dP* (P-P0) + dr/dT* (T-T0) + dr/dC* (C-C0)]
In SEAWAT, we assume that density is not affected by pressure or temperature, and that the reference density is freshwater with a concentration of zero
  r = r f + dr/dC * C
  DENSE = DENSEREF + DENSESLP * CONC
Value for dr/dC is about 0.7143 (25/35) for a freshwater-seawater mixture, if density and concentration are expressed in equivalent units
Note: parts of this taken from Kipp (1987), Kolditz et al. (1998) and Diersch and Kolditz (2002)

## Slide 20: Coupled Flow and Transport
Groundwater flow is affected by fluid density
  q = f(r,…)
Concentration is affected by flow velocity (advection and dispersion)
  C = f(q,…)
Fluid density is function of solute concentration
  r = f(C)

## Slide 21: Solute Transport Processes
Physical Transport of solute
  Advection
  Diffusion
  Mechanical Dispersion
Reactive Transport
  Geochemical reactions
  Biological reactions

## Slide 22: Advection
Transport of solute in flowing groundwater with average groundwater velocity
In most cases, advection is primary process for solute transport

## Slide 23: Dispersion
v  t2
vt1
Spreading of a solute over a greater area than would be predicted solely from average groundwater velocity
Longitudinal dispersion
Transverse dispersion

## Slide 24: Molecular Diffusion
Spread of solute caused by concentration gradients
(A) Container with saline water and distilled water separated by a glass plate
(B) Ionic distribution after removal of glass plate
(C) Ionic distribution at time t1 after removal of plate
(D) Final ionic distribution

## Slide 25: Mechanical Dispersion
Spreading of solute as a result of differences in actual velocity and average velocity
Pore Scale
Macro Scale

## Slide 26: Governing Equation for Solute Transport
ADV
DSP
SSM
RCT
Or, as in MT3DMS
ADV
DSP
SSM
RCT

## Slide 27: Heat/Energy Transport (conserve Energy/Mass)
Stored
Conducted and Dispersed
Convected
Sink/Source
RCT(produced/lost)

## Slide 28: Heat transport…
Solute transport…

## Slide 29: MODFLOW-2000
http://water.usgs.gov/software/modflow.html

## Slide 30: List of Packages (included with MF2K version 1.17)
Bold indicates package not compatible with SEAWAT-2000
BAS6 -- Basic Package
BCF6 -- Block-Centered Flow Package
LPF1 -- Layer-Property Flow Package
RIV6 -- River Package
DRN6 -- Drain Package
WEL6 -- Well Package
GHB6 -- General Head Boundary Package
RCH6 -- Recharge Package
EVT6 -- Evapotranspiration Package
CHD6 -- Time-Variant Specified-Head Package
HFB6 -- Horizontal Flow Barrier Package
SIP5 -- Strongly Implicit Procedure Package
SOR5 -- Slice Successive Over-Relaxation Package
PCG2 -- Version 2 of Preconditioned Conjugate Gradient Package
DE45 -- Direct solver
LMG1 -- Multigrid solver (for USGS use only)
STR6 -- Streamflow-Routing Package
ADV2 -- Advective-Transport Observation Package
RES1 -- Reservoir Package (RES is the file type in the MODFLOW name file)
FHB1 -- Flow and Head Boundary Package (FHB is the file type in the MODFLOW name file)
IBS6 -- Interbed Storage (subsidence) Package (IBS is the file type in the name file)
HUF2 -- Hydrogeologic-Unit Flow Package
LAK3 -- Lake Package
ETS1 -- Evapotranspiration with a Segmented Function Package
DRT1 -- Drains with Return Flow Package
LMT6 -- Link to MT3DMS contaminant-transport model
MNW1 -- Multi-Node Well Package
DAF1 -- Diffusion Analogy Surface-Water Flow Package
SUB1 -- Subsidence and Aquifer-System Compaction Package
SFR2 -- Stream-Flow Routing Package, version 2
GMG1 -- Geometric MultiGrid Solver Package

## Slide 31: Discretization File
NLAY, NROW, NCOL, NPER, ITMUNI, LENUNI
Existence of Quasi-3D Confining Units
DELR
DELC
TOP elevation of system
Bottom elevation of each model layer and Quasi-3D Confining Unit
PERLEN, NSTP, TSMULT, SS/TR for each stress period
  Mixed steady-state and transient simulations
Courtesy Arlen Harbaugh

## Slide 32: Temporal Discretization
Stress periods
Time steps
In MODFLOW2000, stress periods may be either steady-state or transient
STRESS PERIOD 2
(TR)
time
STRESS PERIOD 1
(SS)
STRESS PERIOD 3
(TR)
ts1
ts1
ts2
ts3
ts1
ts2
ts3
ts4
ts5

## Slide 33: LPF Package
Substitute for Block-Centered Flow (BCF)
Internally LPF works like BCF
  Layers are confined or convertible
  Transmissivity, storage, and vertical leakage are based on saturation for convertible layers
  Wetting and drying
Grid independent hydraulic properties
  Specific storage when confined
  Horizontal K even for confined layers
  Vertical K or horizontal to vertical anisotropy ratio
  Vertical K of quasi 3-D confining beds
    NO MORE VCONT

## Slide 34: MT3DMS User Manual
http://hydro.geo.ua.edu/mt3d/mt3dmanual.pdf

## Slide 35: MT3DMS Supplemental Guide

## Slide 36: Solution of the Transport Equation
Fundamental difficulty: the need to treat simultaneously the first-order (hyperbolic) advection term and the second-order (parabolic) dispersion term
ADV
DSP
SSM
RCT
first order
second order
Courtesy Chunmiao Zheng

## Slide 37: Solution Methods
Eulerian
  Fixed grid (standard finite difference or finite element)
Lagrangian
  Deforming grid or deforming coordinate in a fixed grid (particle based)
Mixed Eulerian-Lagrangian
  Combination of Eulerian and Langrangian methods

## Slide 38: Solution Schemes (advection term)
Standard finite difference
  Upstream weighting
  Central-in-space weighting
Method of characteristics
Modified method of characteristics
Hybrid method of characteristics
3rd-order total-variation diminishing (TVD) [ultimate]
Courtesy Chunmiao Zheng

## Slide 39: Courant Number
Number of cells, or fractional cell distance, that a particle is advected in one timestep

## Slide 40: Method of Characteristics (MOC)
Each particle carries a volume and a concentration
Courtesy Chunmiao Zheng

## Slide 41: Advantages and Limitation of Particle Methods
Advantages
  Virtually eliminate numerical dispersion
  Computationally efficient for highly advection-dominated problems
Disadvantages
  May have mass balance discrepancy problems, particularly when model grid is highly irregular
  Calculated concentration breakthrough curves may be “rough”
  Computer memory intensive, particularly for multi-species simulations, with a set of particles for each species
Courtesy Chunmiao Zheng

## Slide 42: Third-Order TVD (ULTIMATE)
Also referred to as higher-order finite-difference or finite-volume method.
TVD—Total Variation Diminishing
ULTIMATE—Universal Limiter for Transient Interpolation Modeling of the Advective Transport Equations
Courtesy Chunmiao Zheng

## Slide 43: Advantages and Disadvantages of TVD
Advantages
  Mass conservative
  Minimal numerical dispersion and artificial oscillation for advection dominated problems
  No numerical difficulty for distorted model grids or in the presence of many sinks/sources
Disadvantages
  Could be computationally demanding
  May not be as effective as MOC in eliminating numerical dispersion for purely advective problems
Courtesy Chunmiao Zheng

## Slide 44: MT3DMS File Structure
Basic Transport Package
Advection Package
Dispersion Package
Sink/Source Mixing Package
Reaction Package
MODFLOW to MT3DMS link file
GCG Solver Package
Basic Output File
Model Configuration File [mt3d.cnf]
Unformatted Concentration File [mt3d001.ucn]
Observation File [mt3d001.obs]
Mass Summary File [mt3d001.mas]
MT3DMS
INPUT
OUTPUT
Courtesy Chunmiao Zheng
Transport Observations Package
Hydrocarbon Spill Source – v. 5.3

## Slide 45: BTN Package
Purpose: to specify
  Basic information
  Spatial discretization
  Boundary and initial conditions
  Printing and saving options
  Temporal discretization
Courtesy Chunmiao Zheng

## Slide 46: Temporal Discretization
Stress periods
Flow timesteps
Transport timesteps
STRESS PERIOD 2
time
STRESS PERIOD 1
STRESS PERIOD 3
ts1
ts1
ts2
ts3
ts1
ts2
ts3
ts4
ts5
1
2
3
4
5
1
2
3
4
1
2
4
3
1
2
4
3
1
1
1
2
1
2
1
2
3
Transport timesteps

## Slide 47: Basic Transport (cont.)
For each stress period
  PERLEN (same as in MODFLOW)
  NSTP (same as in MODFLOW)
  TSMULT (same as in MODFLOW)
  TSLNGTH(NSTP) (only for flow model other than MODFLOW)
  DT0: maximum allowable transport stepsize
  MXSTRN: maximum number of transport steps within one flow timestep
  TTSMULT: transport stepsize multiplier within a flow-model timestep
  TTSMAX: maximum transport stepsize within a flow model timestep (set to zero for no limit)
Courtesy Chunmiao Zheng

## Slide 48: ADV Package
Purpose
  To solve the advection components of the transport equation using one of the following options (through input variable MIXELM)
    Finite Difference
      Upstream weighting
      Central-in-space weighting
    Particle-Based Methods
      MOC
      MMOC
      HMOC
    TVD
Courtesy Chunmiao Zheng

## Slide 49: DSP Package
Purpose: to solve the dispersion component of the transport equation, using the finite-difference technique
Courtesy Chunmiao Zheng

## Slide 50: DSP Package (cont.)
AL (longitudinal dispersivity, unit L)
  Cell-by-cell
  2D array for each model layer
TRPT (ratio of horizontal transverse dispersivity to longitudinal dispersivity)
  One value per model layer
  Input as 1D array for all layers
TRPV
  One value per model layer
  Input as 1D array for all layers
DMCOEF
  One value per model layer
  Input as 1D array for all layers
  D*=tD0
Courtesy Chunmiao Zheng
Can now enter different DMCOEFF for each species (starting in version 5.2)

## Slide 51: Generalized Conjugate Gradient (GCG) Solver
General purpose iterative solver
Three preconditioning options
  Jacobi
  Symmetric Successive Over Relaxation
  Modified Incomplete Cholesky (MIC) (fewer iterations, more memory)
Lanczos/ORTHOMIN acceleration scheme
Two iteration loops (outer loop only required if matrix coefficients are a function of concentration: non-linear sorption)

## Slide 52: SSM Package
Purpose: to solve the source and sink components of the transport equation
Courtesy Chunmiao Zheng

## Slide 53: SSM Package (cont.)
Specify hydraulic sinks/sources
  Point sinks/sources
    Constant-head cells (ITYPE=1)
    Wells (ITYPE=2)
    Drains (ITYPE=3)
    Rivers (ITYPE=4)
    General-head boundaries (ITYPE=5)
    …
    Mass loading (ITYPE=15)
  Distributed sinks/sources
    Recharge
    Evapotranspiration
Courtesy Chunmiao Zheng

## Slide 54: SSM Package (cont.)
What is MXSS?
  The maximum number of POINT sink/source cells (including constant-head cells) used in the flow model. It is only used for memory allocation purposes
How does MT3D know about the cell locations and flow rates of sinks/sources
  Through the flow-transport link file saved by the LMT package in MODFLOW
Courtesy Chunmiao Zheng

## Slide 55: SSM Package (cont.)
Time-varying constant-concentration cell (ITYPE=-1)
  This overrides constant-concentration condition as defined in the BTN input (ICBUND<0)
  Once a cell is defined as ITYPE=-1 it remains a constant concentration cell, but a new concentration value can be specified in different stress periods
Mass-loading source cell (ITYPE=-15)
  Users specify Q*C directly (MT-1)
Courtesy Chunmiao Zheng

## Slide 56: SSM Package (cont.)
Specify concentrations of sinks/sources
  Sinks
    By default, concentration of all sinks set equal to that of aquifer at sink/cell locations
    Default concentration of all sinks cannot be changed except for evapotranspiration
  Sources
    By default, concentration of all sources set equal to ZERO unless specified by user
Courtesy Chunmiao Zheng

## Slide 57: SSM Package
Constant-head vs. constant concentration
  A constant-head cell in MODFLOW is treated as a regular fluid sink/source (like a well). The new inflow/outflow rate through the constant-head cell is determined internally by MODFLOW
  If the constant-head cell acts as a source (inflow), the source concentration is zero unless specified by the user in SSM input. If it acts as a sink (outflow), the sink concentration is always equal to that of the aquifer
  A constant-head cell can be specified as a constant-concentration if so desired
Courtesy Chunmiao Zheng

## Slide 58: SEAWAT Concept
Combine MODFLOW and MT3DMS into a single program
  Insert MT3DMS into MODFLOW main program
Modify MODFLOW routines to solve the variable-density groundwater flow equation

## Slide 59: SEAWAT Processes
Global (GLO) Process
Ground-Water Flow (GWF) Process
Variable-Density Flow (VDF) Process
  Viscosity (VSC) Package
Integrated MT3DMS Transport (IMT) Process
Observation (OBS) Process
Sensitivity (SEN) Process
Parameters Estimation (PES) Process

## Slide 60: Simulation Modes
 | Transport Excluded | Transport Included
Constant Density | GWF | GWF + IMT
Variable Density | VDF | VDF + IMT (uncoupled) VDF + IMT (coupled)

## Slide 61: Optional Simulation Mode: VDF without Transport
User enters 3D array of fluid density
Caution—assumption is that fluid density will not change during the simulation period
Advantage: simulations run quickly because not limited by stability requirements for transport equation

## Slide 62: Spatial Discretization
Information must be consistent between MODFLOW and MT3D
Higher level of vertical discretization required for variable-density groundwater flow (rule of thumb—~10 layers per aquifer)

## Slide 63: Temporal Discretization
Stress periods
Flow timesteps
Transport timesteps
Flow and transport equations solved for each transport timestep
STRESS PERIOD 2
time
STRESS PERIOD 1
STRESS PERIOD 3
ts1
ts1
ts2
ts3
ts1
ts2
ts3
ts4
ts5
1
2
3
4
5
1
2
3
4
1
2
4
3
1
2
4
3
1
1
1
2
1
2
1
2
3
Transport timesteps

## Slide 64: Options for Coupling Flow and Transport
Explicit—one timestep lag
  Works well for most problems
Iterative—repeat solutions until convergence on fluid density
  Can only be used if transport is solved using implicit finite difference
  Can be time consuming and doesn’t seem to help with accuracy for problems tested thus far

## Slide 65: Time-Variant Constant-Head Package
Constant heads read as h and converted to hf for use in the flow equation
Works same as for constant-density MODFLOW simulations

## Slide 66: Options for Specifying Constant Head Boundaries
Set in BAS6
  hf calculated from h and starting concentrations. hf held constant for simulation
  Can’t change h during simulation
Set in CHD Package
  hf calculated from temporally interpolated h and simulated concentration
  Issue with MT3DMS boundary (ITYPE=1)

## Slide 67: Options for CHD Boundaries

## Slide 68: Name File
Name file is requested when SEAWAT Version 4 runs
Contains filetype, unit number, filename
Contains file information for:
  MODFLOW-2000 files
  MT3DMS files
  Variable-Density Flow (VDF) input file
  Viscosity Package (VSC) input file [optional]
FloPy creates valid SEAWAT Version 4 name file

## Slide 69: Example Name File

## Slide 70: VDF File (cont.)
FOR EACH SIMULATION
0. [#Text]
Item 0 is optional and the symbol # must be in column 1. Item 0 can be repeated multiple times, but it cannot be used in the file after the first data record.
1. MT3DRHOFLG MFNADVFD NSWTCPL IWTABLE
2. DENSEMIN DENSEMAX
Read Item 3 if NSWTCPL > 1 or NSWTCPL = -1
3. DNSCRIT
Read Item 4 if MT3DRHOFLG ≥ 0
4. DENSEREF DRHODC(1)
Read Item 4a through 4c if MT3DRHOFLG = -1
4a. DENSEREF DRHODPRHD PRHDREF
4b. NSRHOEOS
4c. MTRHOSPEC(NSRHOEOS) DRHODC(NSRHOEOS) CRHOREF(NSRHOEOS)
Item 4c is read as a table, with one row representing each MT3DMS species to be included in the equation of state for fluid density. There is no requirement that this table be sorted by MTRHOSPEC.
5. FIRSTDT
FOR EACH STRESS PERIOD
Read Items 6 and 7 only if MT3DRHOFLG = 0
6. INDENSE
Read Item 7 only if INDENSE is greater than zero
7. [DENSE(NCOL,NROW)] – U2DREL
Item 7 is read for each layer in the grid.

## Slide 71: DENSEREF and DENSESLP
Concentration |  | 
units | freshwater | seawater
mg/L | 0 | 35,000
g/L | 0 | 35
lbs/ft3 | 0 | 2.188
relative | 0 | 1
Density |  | 
units | Freshwater (DENSEREF) | seawater
g/cm3 | 1 | 1.025
kg/m3 | 1000 | 1025
lbs/ft3 | 62.42 | 63.98
Example:
use concentration in mg/L and density in kg/m3
Density length units must be same as length units used for model grid, hydraulic conductivity, etc.

## Slide 72: Density Equation of State
Multiple-species
Temperature
Water Compressibility

## Slide 73: VSC Input File
By including in name file will activate the VSC option
VSC file is created by FloPy
Have multiple options from manual
  Concentration
  Temperature

## Slide 74: VSC File
FOR EACH SIMULATION
0. [#Text]
Item 0 is optional and the symbol # must be in column 1. Item 0 can be repeated multiple times.
1. MT3DMUFLG
2. VISCMIN VISCMAX
Read item 3 if MT3DMUFLG ≥ 0
3. VISCREF DMUDC(1) CMUREF(1)
Read item 3a through 3c if MT3DMUFLG = -1
3a. VISCREF
3b. NSMUEOS MUTEMPOPT
3c. MTMUSPEC(NSMUEOS) DMUDC(NSMUEOS) CMUREF(NSMUEOS)
Item 3c is read NSMUEOS times, once for each MT3DMS species to be included in the viscosity equation.
3d. MTMUTEMPSPEC AMUCOEFF(MUNCOEFF)
Item 3d is read if MUTEMPOPT > 0. The size of the AMUCOEFF coefficient array depends on the selected equation for viscosity.
FOR EACH STRESS PERIOD
Read items 4 and 5 only if MT3DMUFLG = 0
4. INVISC
Read item 5 only if INVISC is greater than zero
5. [VISC(NCOL,NROW)] – U2DREL
Item 5 is read for each layer in the grid.

## Slide 75: Constitutive Relation for Viscosity
or
e.g. SUTRA
MUTEMPOPT
1
2
3

## Slide 76: Special Considerations for Packages
All input and output is expressed in terms of head (not equivalent freshwater head)
All storage and hydraulic properties must be represented in terms of equivalent freshwater values (or relative to the reference density)

## Slide 77: Model Results of Interest
Listing Files
  Flow budget
  Solute mass budget
Heads
Flows
Concentrations
  Unformatted concentration file
  Concentration observations
Solute mass budget

## Slide 78: Flow Budget

## Slide 79: Solute Budget